SurvivorSurvivor Helicopter!

Level Data Format

Open Game Developers

[Version: 0.0.0.1]	[Date: 05|08|2013]

Change Log

Version	Author	Changes
0.0.0.1	El-Rico	A first-adjustment pass of the level file format

###### Table of Contents

###### Preface

This document exists to detail the particulars of the level format used for SurvivorSurvivor Helicopter! Level formations will not be described in this document, see the Level Designs Document for more information on the levels used in the game.

###### Anatomy of a Level

Components
Tiles are assumed to be meshes in the ZED mesh file format.

Tile ID
An 8-bit value which provides more than enough variety in tiles for a single level.

Tile flags
An 8-bit value, which indicates whether this tile is a spawn point or if it is a helicopter landing zone.

File Layout

Type		Count	Name	Description
char		4	ID	Contains “SSHL” (SurvivorSurvivor Helicopter! Level)
char		256	Path	Path to the tile set
Unsigned 16-bit integer		2	Dimensions	The width and depth of the level, respectively
for width*height
	byte	1	Tile ID	The tile to use (tile sets contain meshes with names starting at zero, zero and one are reserved for the spawn point tile and the helicopter landing zone tile, respectively)
	byte	1	Tile Flags	Eight OR-ed flags which determines the type of tile this is
end for

Loading a Level
Pseudocode
read file_header	;((char*4)+(char*256)+(uint16*2))
if compare( file_header.id, “SSHL” ) not successful
return;
if failed( check_tile0_and_tile1_are_present( file_header.path ) )
return;
if failed( check_all_tiles_in_file_exist( file_header.path ) )
return;
store_tile_ids_in_order_with_index( )	;Takes the tile IDs from the previous check and
 ;stores them in a list so that the renderer
;doesn't need to keep switching meshes and
;textures as often

Rendering a Level
Pseudocode
for( x = 0; x < tile_id; ++x )
itr = tile_id_position_map[ x ].begin	;tile_id_position_map = map< int, list > - The list contains all	;of the positions for the tile
while( itr != tile_id_position_map[ x ].end )
render_tile( x, itr.position )